## Slide 1: GAMS OPTIMIZATION INTRODUCTION FOR STARTERS

## Slide 2
GAMS INTRODUCTION
INPUT TEXT FILES
GAMS MODEL COMPILATION
OUTPUT FILES
OPTIMIZATION SOLVER
The General Algebraic Modelling System (GAMS) is a high level modeling system for mathematical programming and optimization

## Slide 3
SIMPLE RECYCLE OPTIMIZATION PROBLEM

## Slide 4: CONTENTS
What is GAMS?
GAMS Development
GAMS in Process Optimization
GAMS Editors
GAMS IDE
Introduction to GAMS IDE Interface
GAMS Studio
Introduction to GAMS Studio Interface
Examples of GAMS Model

## Slide 5: WHAT IS CRUDE OIL?
Crude oil is a liquid fuel source located underground.
Crude oil is also called a fossil fuel because of its origins. It is formed when great amount of dead organisms(algae & zooplankton) are buried beneath sedimentary rocks and then subjected to heat and pressure.
The intense pressure heated them over millions of years. It first became a waxy substance called kerogen. It became liquid oil after more pressure and heat which makes it a nonrenewable resource.
It has between 50 and 97 percent of oil, hydrocarbons. Between 6 to 10 percent of nitrogen, oxygen, and sulfur.

## Slide 6
How Crude Oil Actually Looks Like…
Crude oil doesn't always look the same, it depends where it comes from. Sometimes it is almost colourless, or it can be thick and black. But crude oil usually looks like thin, brown treacle.

## Slide 7
Crude oil classification
Location
Brent
WTI (West TExas intermidiates)
Sulphur Content
SWEET: Sweet crude oil has little sulphur content (<1wt%).
Sour: Sour crude oil has a considerable sulphur content (>1%wt).
API GRAVITY
LIGHT: Low density.
MEDIUM: Range of low and high density.
HEAVY: High density

## Slide 8: Crude oil composition

## Slide 9
Crude oil ASSAY AND BLEND
Chemical evaluation of crude oils feedstock by petroleum testing laboratories gives the assay data of oils. Each crude oil type has unique molecular and chemical characteristics.
The results of crude oil assay testing provide extensive detailed hydrocarbon analysis data for refiners, oil traders and producers.
Assay data help refineries determine if a crude oil feedstock is compatible for a particular petroleum refinery or if the crude oil could cause yield, quality, production, environmental and other problems.
A blend is a mixture of crude oils, blended in the pipeline to create oil with specific physical and chemical properties.
Crude oil blending is often undertaken to increase the sale price or process-ability of a lower grade crude oil by blending it with a higher grade, higher price crude.

## Slide 10
CRUDE OIL CHARACTERIZATION and Properties
Crude oils are characterized to determine their properties through analysis.
Crude oils characterization is a means evaluating selected physical and chemical properties of crude oils
These properties are used for identifying the crude oils output layer, estimating the sedimentary environment and the origin of their organic matter from the source rocks, evaluating their processing methods, and checking the quality of oil for commercial sale and modeling of their reservoirs.
The selected physical and chemical properties to be analyzed and evaluated includes the followings:
Boiling point
Specific/API gravity
Light ends
Molecular weight
Sulphur content
Viscosity
Flash point
Freeze point
Other petroleum properties.

## Slide 11
Boiling Point
It is the temperature at which the vapour pressure of the liquid equals the pressure surrounding the liquid. As a result, the liquid change phase to vapour.
There are several methods of measuring and reporting boiling points (distillation curves) of crude oil, some common ones are:
True Boiling Point (TBP)
ASTM D86
Simulated Distillation (SD) or ASTM D 2887
Equilibrium Flash Vaporization\ASTM D1160
Vacuum

## Slide 12
Boiling Point
The difference between final boiling point (FBP) and initial boiling point (IBP) is called boiling ranges.
Crude oils with wider boiling ranges contain more compounds than the one with narrower boiling ranges.
Crude oils have boiling ranges of more than 550 Celsius.
Using crude oil FBP is not accurate in ascertaining the purity of different oil.
Rather, normal boiling point of each oil cut boiling ranges is used.
Atmospheric true boiling point (TBP) data are obtained through distillation of oil using a distillation apparatus with 15-100 theoretical plates at relatively high reflux ratios (1-5 or aggregate).
The high degree of fractionation in these distillations gives accurate component distributions for crude mixtures.

## Slide 13
API/specific GRAVITY
Both API gravity and specific gravity are measure of density of the crude oil.
API Gravity
It’s usually measured at 60 degree Fahrenheit.
Higher value implies more light components of the crude oil .
It can also be used to calculate the approximate barrels per metric ton of oil.
Specific Gravity
Specific gravity is calculated as the ratio of the density of a liquid to the density of water.
Specific gravity of oil generally lies in between 0.73 and 0.84 or very slightly greater.
It is formally express in degrees of the European Beaumè scale read directly hydrometer, this means the S.G increase as the density goes up i.e. heavy oil has high specific gravity

## Slide 14
LIGHT ENDS
Assay data of certain crude oils, especially light crudes, may contain detailed analysis of defined components, such as methane through n-hexane.
The percent composition of these component is found through light end distillation test of oil assays or gas chromatography.
With these data, each of these components can treated as standard chemical compound component during the overall assay characterization process.

## Slide 15
Molecular Weight
This is the average weight of a molecule of an element or compound measured based on 1/12 the weight of carbon 12.
Molecular weight of a crude can be estimated through the determination of the mole fraction of all components and their corresponding weight then summing up.
Cragoe correlation can be used.
MW = (6084/API- 5.9)

## Slide 16
Sulphur Content
Amount of Sulphur (usually inorganic) present in the crude oil.
This can be sued for the classification of crude oil i.e. its grade.
Sweet oil has Sulphur content less than 1 wt.%
Sour crude has Sulphur content greater than 1 wt.%
Sweet crude is usually desired.
Sulphur content of oil is required to prevent the adverse effect (e.g. during refining )
It can be carried out using ASTM D129 Test (i.e. for low volatile petroleum Product)

## Slide 17
Viscosity
Viscosity is the internal friction of fluid causing it resistant to put change of form. (viscosity is conventionally written in a Greek letter eta, η).
It is the ratio of stress to shear per unit time. Shear with liquid is not a constant but is proportional to time.
Viscosity = Force*Distance/Area*Velocity.
The higher the viscosity, higher the resistance to flow.
It could be kinematic (measured with viscometers ) or dynamic.
The CGS unit of viscosity is the poise which is too larger unit of practical purpose in the oil industry. Viscosity of oil are therefore conventionally measured in centipoises.

## Slide 18
FLASH POINT
The lowest temperature at which crude oil gives off sufficient vapour to ignite in the air given an ignition source.
It indicates flammability or combustibility.
The flash point is different from boiling point.
It is determined for safety purpose in processing operation.
The analysis is usually carried out using flash point testet.

## Slide 19
FREEZE POINT
This is the temperature at which liquid solidifies at 1 atmospheric pressure for pure compound.
For the crude oil, it ranges from -40 degree Fahrenheit to -60 degree Fahrenheit.
It’s also important for the transportation of crude oil.

## Slide 20
OTHER PETROLUEM PROPERTIES
Pour Point
Refractive Index
Carbon Residue
Research Octane Number (RON)
Cloud Point
Smoke Point
Cetane Number
Paraffin Content
Bromine Number
Reid Vapour Pressure
Aniline Point
Olefin Content
Mercaptan Content etc.

## Slide 21
Characterization of Nigerian crude blends with aspen plus